## Slide 1: Innovative Design and Optimization of Arithmetic Circuits in Quantum Computing
Siyi Wang siyi002@e.ntu.edu.sg College of Computing and Data Science

## Slide 2
Siyi Wang
PhD Candidate, CCDS
Research Focus
Quantum Computing
Quantum Cryptography

## Slide 3
Arithmetic Designs
Preliminaries
Hardware Validation
Content
01
Background
02
03
04
Applications
Conclusion
05
06

## Slide 4
The beginning of this story......
01
Background
From ancient Greece,
people were already curious about Atoms.
Ancient Greece

## Slide 5
5th Solvay Conference on Quantum Mechanics, 1927.
Quantum Mechanics
Computing
History of Computing.
Quantum Computing
Quantum Mechanics and Computing

## Slide 6
The development of quantum Computing
1981
Richard Feynman proposed quantum computing in his talk.
2011
First commercial Computer
D-Wave One.
2024
Google's Willow Quantum Chip.

## Slide 7
Cryptography
Quantum computers promise breakthroughs across domains by offering speedups over classical algorithms. A landmark example is Shor’s algorithm[1], which threatens public-key cryptographic systems such as RSA and ECC.
Quantum arithmetic serves as a basic building block in many quantum algorithms. In particular, the efficiency of Shor’s algorithm[1] relies heavily on arithmetic blocks.
Drug Discovery
Finance
Quantum Computer
Quantum Computing

## Slide 8
Research Gap
However...
Narrow focus: Existing work primarily optimizes arithmetic circuits for specific problems only.
Unexplored areas: Important topics like modular arithmetic and division remain under-investigated.
Absence of general framework: No general, systematic methodology exists for designing quantum arithmetic blocks.
Missing comprehensive survey: An up-to-date, thorough review of this field is still lacking.
Some work has already been conducted on quantum arithmetic.

## Slide 9
Research Question
How to improve the efficiency of Quantum Arithmetic?

## Slide 10
Expensive!
02
Preliminaries
Classical Bit
Distinct States
Quantum Bit (Qubit)
States Simultaneously
Bit vs. Qubit
OR
All Apples Filled
All Apples Empty

## Slide 11
Quantum Gates
Here is a concise overview of basic quantum logic gates, including corresponding quantum circuits as well as unitary matrices.
Expensive!
Classical Logical Gates
Quantum Logical Gates
AND
OR
NOT

## Slide 12
Most Expensive Quantum Resources
Toffoli Gate
Qubit
Toffoli-Depth (TD)
Toffoli-Count (TC)
Qubit-Count (QC)
Main
Metrics
Evaluation Metrics

## Slide 13
03
Arithmetic Designs
MOD
Previous
Designs
There are several strong works exist, but...

## Slide 14
✓
↓ Qubit-Count
✓
↓ Toffoli-Count (7*2→ 4)
↓ Toffoli-Depth (3*2→ 2)
✓
Our Exploration!
Addition
Computation
Uncomputation
Computation[2]
Uncomputation[2]
Strategy 1
Strategy 2
→

## Slide 15
Design Choice 1: Radix
Quantum Higher Radix Adder
✓
✓
✓
✓
✓

## Slide 16
Using the higher radix to reduce T-depth and overall time cost.
Radix 2
(Default)
Radix 3
Radix 4
4
3
2
What is Radix？

## Slide 17
Our Design
Example
Radix=3
Addition Size=15
Carry Path
Sum Path
Higher
Radix
Structure
Initialization
Radix 3
General Framework
Higher Radix Structure

## Slide 18
Performance of Our Design
Zoom in on the gray scope
TD
QC
TC
TD
QC
TC
Our work can be seen as a bridge to connect existing quantum adders.

## Slide 19
Design Choice 2: Propagation & Generation Method
✓
✓
✓
✓
✓

## Slide 20
Ling structure can reduce T-depth sharply.
5
3
O(2log2n)
O(2log2(n/2))
What is Ling-based Propagation & Generation Method？
General Method
Ling-based Method

## Slide 21
Our Design (Example: Addition Size=4)
Ling Initialization
Ling Pre-calculation
Ling Propagation & Generation
Sum
Uncompute Propagation & Generation
Uncompute Initialization
Similar to Carry Path
Similar to Sum Path

## Slide 22
Performance of Our Design
TD Comparison
TC Comparison
QC Comparison
Our design achieves a reduced TD of O(log (n/2)), improving over other Q adders with O(log n) TD.
[3]
[4]
[5]

## Slide 23
Design Choice 3: Prefix Tree
✓
✓
✓
✓
✓
✓

## Slide 24
What is Prefix Tree?
Choice of Classical Prefix Tree
Quantum Brent-Kung (Default)
A tree structure that efficiently computes carry signals by combining intermediate results in parallel.
Quantum Kogge-Stone
Quantum Han-Carlson
Quantum Sklansky
Quantum Ladner-Fischer
Brent-Kung
Quantum
Add
Are we the perfect match?
✓

## Slide 25
Our Design
Optimal Depth Add= Sklansky Tree + In-place + With Uncomputation+ Toffoli Strategy 2
Pre-calculation
Carry Propagation & Generation
CNOT operations, with numbers in circles indicating the number of CNOT operations.
Initialization
Carry Path
(Sklansky)
Uncomputation
Sum Path
Sklansky Tree

## Slide 26
Performance of Our Design
TD Comparison
TC Comparison
QC Comparison

## Slide 27
Subtraction
An n-bit quantum subtractor can be built with minor modifications to an n-bit quantum adder.
Method 1
Method 2
Cost Comparison

## Slide 28
Division
Non-Standard Evaluation!
Fast division is slow in quantum???
Slow Division
  Restoring
  Non-Restoring
  ...
Fast Division
  Newton–Raphson
  Goldschmidt
  ...
Division
Algorithm
Quantum
Division
Designs
Slow Division
  Restoring(2019, Thapliyal et al.[89])
  Non-Restoring(2019, Thapliyal et al.[89])
  ...
Fast Division
  Newton–Raphson(2022, Gayathri et al.[90])
  Goldschmidt(2021, Gayathri et al.[69])
  ...
Our Division Design
Corrected!
Comparison of 32-qubits Quantum Dividers
Yes! Because Quantum IF is very expensive!

## Slide 29
Multiplication
Schoolbook or shift-and-add methods often yield better Qubit-Count.
Compare to existing Wallace Tree Quantum Multipliers:
Lower Toffoli-Count ↓
Lower Toffoli-Depth ↓
Comparable Qubit-Count
Half Adder
Full Adder
Basic Primitives
Compressor Primitives

## Slide 30
Modular Arithmetic (MOD)
Modular Addition
VBE Modular Addition Framework[25]
Beckman Modular Addition Framework[26]
Van Meter Modular Addition Framework[27]
Rines-Chuang Modular Addition Framework[28]
a+b-N

## Slide 31
High-Speed, Low-Cost with Low Latency
  Minimizes delay by avoiding the need for immediate carry propagation.
Efficient Multi-Operand Addition
  Reduces the time required for multi-operand additions.
Why Use Carry-Save Architecture?
Based on Addition Block
Our Design

## Slide 32
Modular Addition Framework | Year | TD | TC | QC
VBE[25] | 1996 |  |  | 
Beckman[26] | 1996 |  |  | 
Van Meter[27] | 2005 |  |  | 
Rines-Chuang[28] | 2018 |  |  | 
Our Design | 2024 |  |  | 
Modular Addition Framework | Year | TD | TC | QC
VBE[25] | 1996 |  |  | 
Beckman[26] | 1996 |  |  | 
Van Meter[27] | 2005 |  |  | 
Rines-Chuang[28] | 2018 |  |  | 
Our Design | 2024 |  |  | 
Theoretically, our design achieves the lowest TD
Performance of Our Design
Chart: 
| 第一季度 | 第二季度
销售额 | 2 | 8
33.3%
Improve TD (Time) of
Quantum Modular Framework
Chart: 
| 第一季度 | 第二季度
销售额 | 6 | 4
60%
Improve TD (Time) of
Quantum Exponentiation
Lowest Toffoli Depth
Shor’s Acceleration

## Slide 33
Overview
We had an overview paper for quantum arithmetic, which has been published by Philosophical Transactions of the Royal Society A.
Isaac Newton

## Slide 34
How can we verify these designs?
NISQ device has 50–100 qubits, capable of limited quantum advantage despite error and noise constraints.
Noisy intermediate-scale quantum(NISQ) computer
We are Here!
Quantity
Quality
04
Hardware Validation

## Slide 35
Validation Flow
...
Quantum
Simulator
Quantum
Hardware
Design
Programming
Verification

## Slide 36
Industry Attention
Our Design!
Our designs have been incorporated into recent quantum algorithm APIs. It’s encouraging to see growing interest from the industry in our work.

## Slide 37
MalaQ: The first Malware for Quantum Computers
The technological revolution ushered in by quantum computers has garnered widespread attention, rendering quantum machines the likely targets of cyber attacks.
Therefore,
we propose the 1st Malware Demo for Quantum Computer---MalaQ
Quantum Computer in NUS

## Slide 38
Quantum Computer Cybersecurity Symposium 2024
Our Work!
SWE@NTU Research Showcase 2025
Recognition & Impact

## Slide 39
Quantum
Arithmetic Circuits
Quantum
Machine Learning
Aimed at achieving a comprehensive exploration of the quantum domain from bottom to top.
Q Arithmetic
QML
Q Crypt
......
Quantum
Cryptanalysis
......
05
Applications

## Slide 40
Application 1: Quantum Machine Learning
Quantum Trick
Simultaneous execution of shared-control Toffoli
There are no quantum designs for implementing activation functions with a focus on fault tolerance so far.
ReLU
Leaky ReLU
Performance
Our implementations achieve constant T-depth.

## Slide 41
In symmetric-key cryptography, Grover's Attack[29] poses the primary security threat.
Application 2: Quantum Cryptanalysis
Quantum Oracles for Grover’s Attack
LED-64
LED-128

## Slide 42
In conclusion, my PhD research improved the efficiency of quantum arithmetic, thereby advancing various quantum applications and large-scale algorithms.
Quantum Arithmetic
Hardware Validation
Applications
06
Conclusion
Addition
Subtraction
Multiplication
Division
Modular Arithmetic
Overview
Verification
Malware Design
Q Machine Learning
Q Cryptanalysis

## Slide 43
Classical → Quantum
Classical techniques inspire quantum arithmetic designs
Quantum → Quantum Innovations in one quantum design inform others
Bridge classical and quantum computing
Research Question: How to improve the efficiency of Quantum Arithmetic?
Our Answer
The connection between classical and quantum computing is indispensable.

## Slide 44
List of Publications
Journal Papers
Wang, Siyi, Anubhab Baksi, and Anupam Chattopadhyay., (2023) "A Higher radix architecture for quantum carry-lookahead adder." Scientific Reports 13, no. 1: 16338.10.1038/s41598-023-41122-4
Wang, Siyi, Ankit Mondal, and Anupam Chattopadhyay., (2024) "Optimal Toffoli-Depth Quantum Adder." ACM Transactions on Quantum Computing,10.1145/3743691.
Wang, Siyi, Xiufan Li, Wei Jie Bryan Lee, Suman Deb, Eugene Lim, and Anupam Chattopadhyay., (2024) "A Comprehensive Study of Quantum Arithmetic Circuits." Philosophical Transactions of the Royal Society A, 10.1098/rsta.2023.0392
Zi, Wei, Siyi Wang, Hyunji Kim, Xiaoming Sun, Anupam Chattopadhyay, and Patrick Rebentrost., (2024) "Efficient quantum circuits for machine learning activation functions including constant T-depth ReLU." Physical Review Research 6, no. 4: 043048, 10.1103/PhysRevResearch.6.043048.
Book Chapter
Wang, Siyi, and Anupam Chattopadhyay.(2023) "Efficient Depth Optimization in Quantum Addition and Modular Arithmetic with Ling Structure." IFIP/IEEE International Conference on Very Large Scale Integration-System on a Chip. Cham: Springer Nature Switzerland, 2023.

## Slide 45
List of Publications
Wang, Siyi, and Anupam Chattopadhyay., (2023) "Reducing depth of quantum adder using ling structure." 2023 IFIP/IEEE 31st International Conference on Very Large Scale Integration (VLSI-SoC), 561–566. 10.1109/VLSI-SoC57769.2023.10321948
Wang, Siyi, Eugene Lim, and Anupam Chattopadhyay., (2024) "Boosting the Efficiency of Quantum Divider through Effective Design Space Exploration." 2024 IEEE International Symposium on Circuits and Systems (ISCAS), 10.1109/ISCAS58744.2024.10557991.
Wang, Siyi, Eugene Lim, Xiufan Li, Jerrie Feng, and Anupam Chattopadhyay., (2024) "Minimum Depth Quantum Modular Addition through Carry-Save Architecture", 2024 IFIP/IEEE 32st International Conference on Very Large Scale Integration (VLSI-SoC), 10.1109/VLSI-SoC62099.2024.10767796 (Best Paper Award)
Wang, Siyi, Alex Jin, Suman Deb, Tarun Dutta, Manas Mukherjee, and Anupam Chattopadhyay., (2024) "POSTER: MalaQ-A Malware Against Quantum Computer." In Proceedings of the 19th ACM Asia Conference on Computer and Communications Security, 10.1145/3634737.3659432. (Best Student Presentation Award)
Wang, Siyi, Kyungbae Jang, Anubhab Baksi, Sumanta Chakraborty, Bryan Lee, Anupam Chattopadhyay and Hwajeong Seo., (2024) "New Results in Quantum Analysis of LED: Featuring One and Two Oracle Attacks" IACR Communications in Cryptology, Under review.
Conference Proceedings

## Slide 46
Acknowledgment
Prof. Anupam Chattopadhyay
Thesis Committee
Prof. Pun Chi Seng Prof. Wang Yong Prof. Tao Dacheng

## Slide 47
Acknowledgment
Family, Friends, and Coworkers...

## Slide 48: Q&A Thank you for listening!

## Slide 49
References
[1] Shor, P.W., 1999. Polynomial-time algorithms for prime factorization and discrete logarithms on a quantum computer. SIAM review, 41(2), pp.303-332.
[2] Gidney, Craig. Halving the cost of quantum addition. Quantum, 2:74, June 2018. ISSN 2521-327X. doi: 10.22331/q-2018-06-18-74. URL https://doi.org/10.22331/q-2018-06-18-74.
[3] T. Draper, S. Kutin, E. Rains, and K. Svore, “A logarithmic-depth quantum carry-lookahead adder,” Quantum Information and Computation, vol. 6, 07 2004.
[4] Y. Takahashi and N. Kunihiro, “A fast quantum circuit for addition with few qubits,” Quantum Information and Computation, vol. 8, pp. 636–649, 07 2008.
[5] Y. Takahashi, S. Tani, and N. Kunihiro, “Quantum addition circuits and unbounded fan-out,” Quantum Information and Computation, vol. 10, 10 2009.
[6] S. S. Gayathri, R. Kumar, S. Dhanalakshmi, G. Dooly, and D. B. Duraibabu, “T-count optimized quantum circuit designs for single-precision floating-point division,” Electronics, vol. 10, p. 703, 03 2021.
[7] S. S. Gayathri, R. Kumar, and S. Dhanalakshmi, “Efficient floating-point division quantum circuit using newton-raphson division,” Journal of Physics: Conference Series, vol. 2335, no. 1, p. 012058, sep 2022. [Online]. Available: https://dx.doi.org/10.1088/1742-6596/2335/1/012058
[8] C. Zalka, “Fast versions of shor’s quantum factoring algorithm,” arXiv preprint quant-ph/9806084, 1998.
[9] A. Parent, M. Roetteler, and M. Mosca, “Improved reversible and quantum circuits for karatsuba-based integer multiplication,” arXiv preprint arXiv:1706.03419, 2017.
[10] C.-C. Lin, A. Chakrabarti, and N. K. Jha, “Qlib: Quantum module library,” ACM Journal on Emerging Technologies in Computing Systems (JETC), vol. 11, no. 1, pp. 1–20, 2014.

## Slide 50
References
[11] S. Kepley and R. Steinwandt, “Quantum circuits for f _ 2ˆ n f 2 n-multiplication with subquadratic gate count,” Quantum Information Processing, vol. 14, pp. 2373–2386, 2015.
[12] H. Jayashree, H. Thapliyal, H. R. Arabnia, and V. K. Agrawal, “Ancilla-input and garbage output optimized design of a reversible quantum integer multiplier,” The Journal of Supercomputing, vol. 72, pp. 1477–1493, 2016.
[13] S. Dutta, D. Bhattacharjee, and A. Chattopadhyay, “Quantum circuits for toom-cook multiplication,” Phys. Rev. A, vol. 98, p. 012311, Jul 2018.
[14] E. Muñoz-Coreas and H. Thapliyal, “Quantum circuit design of a t-count optimized integer multiplier,” IEEE Transactions on Computers, vol. 68, no. 5, pp. 729–739, 2018.
[15] C. Gidney, “Asymptotically efficient quantum karatsuba multiplication,” arXiv preprint arXiv:1904.07356, 2019.
[16] C. Gidney, “Windowed quantum arithmetic,” arXiv preprint arXiv:1905.07682, 2019.
[17] I. Van Hoof, “Space-efficient quantum multiplication of polynomials for binary finite fields with sub-quadratic toffoli gate count,” arXiv preprint arXiv:1910.02849, 2019.
[18] H. T. Larasati, A. M. Awaludin, J. Ji, and H. Kim, “Quantum circuit design of toom 3-way multiplication,” Applied Sciences, vol. 11, no. 9, p. 3752, 2021.
[19] S. Gayathri, R. Kumar, S. Dhanalakshmi, G. Dooly, and D. B. Duraibabu, “T-count optimized quantum circuit designs for single-precision floating-point division,” Electronics, vol. 10, no. 6, p. 703, 2021.
[20] S. Sajadimanesh, J. P. L. Faye, and E. Atoofian, “Practical approximate quantum multipliers for nisq devices,” in Proceedings of the 19th ACM International Conference on Computing Frontiers, pp. 121–130, 2022.
[21] D. S. C. Putranto, R. W. Wardhani, H. T. Larasati, and H. Kim, “Space and time-efficient quantum multiplier in post quantum cryptography era,” IEEE Access, vol. 11, pp. 21848–21862, 2023.

## Slide 51
References
[22] F. Orts, E. Filatovas, G. Ortega, J. SanJuan-Estrada, and E. Garzón, “Improving the number of t gates and their spread in integer multipliers on quantum computing,” Physical Review A, vol. 107, no. 4, p. 042621, 2023.
[23] J. Nie, Q. Zhu, M. Li, and X. Sun, “Quantum circuit design for integer multiplication based on schönhage-strassen algorithm,” IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, 2023.
[24] K. Jang, W. Kim, S. Lim, Y. Kang, Y. Yang, and H. Seo, “Quantum binary field multiplication with optimized toffoli depth and extension to quantum inversion,” Sensors, vol. 23, no. 6, p. 3156, 2023.
[25] Vedral, V., Barenco, A. and Ekert, A., 1996. Quantum networks for elementary arithmetic operations. Physical Review A, 54(1), p.147.
[26] Beckman, D., Chari, A.N., Devabhaktuni, S. and Preskill, J., 1996. Efficient networks for quantum factoring. Physical Review A, 54(2), p.1034.
[27] Van Meter, R. and Itoh, K.M., 2005. Fast quantum modular exponentiation. Physical Review A—Atomic, Molecular, and Optical Physics, 71(5), p.052320.
[28] Rines, R. and Chuang, I., 2018. High performance quantum modular multipliers. arXiv preprint arXiv:1801.01081.
[29] Grover, Lov K. A fast quantum mechanical algorithm for database search. In Proceedings of the twenty-eighth annual ACM symposium on Theory of computing, pages 212–219, 1996.

## Slide 52
07
Appendix
Quantum Higher Radix Adder

## Slide 53
Step 2: Pre-calculation
Step 1
Quantum Ling Adder

## Slide 54
CSA Module
Uncompute S Module
Set 0 Module
Add Module
Sub Module
Modular Addition

## Slide 55
represents the carry-save architecture, consisting of a series of full adders operating in parallel.
CSA Module
uncompute the partial sum S,
which can be achieved through CNOTs.
Uncompute S Module
can be implemented using CNOTs.
Set 0 Module
represents a quantum adder.
There are various quantum adders.
Add Module
Method
Main Modules
denotes a quantum subtractor,
which is a direct application of Add.
Sub Module

## Slide 56
Method
Add/Sub Module
Add/Sub | TD | TC | QC
Gayathri[6] |  |  | 
Takahashi[7] |  |  | 
Optimal TD[8] |  |  | 
Add/Sub | TD | TC | QC
Gayathri[6] |  |  | 
Takahashi[7] |  |  | 
Optimal TD[8] |  |  | 

## Slide 57
Results
Experiment 1
Chart: 
| 第一季度 | 第二季度
销售额 | 2 | 8
33.3%
TD(Time)
Improvement
Our Design_Takahashi
Takahashi: low QC Adder
Our Design_Gayathri
Gayathri: low TC Adder
Our Design_OptimalTD
OptimalTD: low TD Adder
TD Comparison

## Slide 58
QC Comparison
TC
Rines-Chuang framework with Gayathri Add achieves the lowest TC cost, with our design closely following as the second lowest.
QC
Our design exhibits a QC that falls slightly below the Beckman framework.
The choice of Add Block and Modular Framework significantly impacts the performance of modular adders.
Our designs exhibit up to 33.3% reduction in TD, while keeping TC and QC at comparable levels.
Discussions
Results
Experiment 1
TC Comparison

## Slide 59
VBE Modular Multiplication Framework[2]
Results
Experiment 2: Influence on Quantum Modular Exponentiation
SETState
Modular Adder

## Slide 60
Chart: 
| 第一季度 | 第二季度
销售额 | 6 | 4
60%
TD(Time)
Improvement
Results
Experiment 2
is an n-bit binary number)
n-bit controlled modular multiplier
VBE Modular Exponentiation Framework[2]

## Slide 61
Quantum Division
Comprehensive application of DSE methodology during quantum divider design

## Slide 63
Results and Discussions

## Slide 64
Results and Discussions

## Slide 65
In contrast, classical arithmetic circuit designs leverage the compressor primitive, having demonstrated superior performance[5,6,7].
Quantum Multiplication
Existing designs of quantum multiplier[2,3,4] often rely on basic half and full-adders as primitives.
Half Adder (HA)
Full Adder (FA)
Basic Primitives (HA, FA)
Our Primitives (Compressors)
Example
10-4 compressor adder using 5-3 compressor adders

## Slide 66
Methodology: Compressor-based Wallace Tree Multiplier
8x8 Wallace Tree multiplication based on B𝐵7
B9 Quantum Compressor

## Slide 67
Experiment: Determining the Optimal Compression Size
We investigate the optimal compression size l using 3 strategies:
Strategy 1: Use the largest possible compressor size.
Strategy 2: Use the largest compressor with maximum compression ratio.
Strategy 3: Brute-force search.
T-Depth Comparision
T-Depth Optimization
Using OptimalTD-Add, Strategy 3 performs best but scales poorly.
For larger N, Strategy 1 outperforms Strategy 2 in minimizing T-Depth.

## Slide 68
Experiment: Determining the Optimal Compression Size
T-Count Comparision
Qubit-Count Comparision
Note
Brute-force optimization is ideal for small-scale multiplications.
For larger circuits, Strategy 1 offers the best balance of performance and scalability.
T-Count Optimization
We adopt OptimalTC-Add as the CPA.
While Strategy 3 (brute-force) yields the lowest T-Count, it is impractical for large N.
In such cases, Strategy 1 (largest compressors) is a practical and efficient alternative.
Qubit-Count Minimization
Naive or shift-and-add methods often yield better Qubit-Count.
Within our framework, Strategy 1 matches or outperforms Strategy 2, while Strategy 3 remains optimal but costly.

## Slide 69
To date, no documented attack has successfully achieved direct control over a quantum computer.
we successfully overcame these challenges, culminating in the development of the first malware targeting quantum computers.
Challenge 1: The complex and unique nature of quantum systems.
Challenge 2: Gap between quantum and cybersecurity
MalaQ

## Slide 70
Methodology: Detailed Step-by-step Breakdown of the Attack
Step1: Design and program a reverse TCP-based malware
Step 2: Delivery MalaQ to the Target CPU
Step 3: Execution MalaQ on the Target CPU
Step 4: Access to the Target System.
Step 5: Attack on Quantum Classifier.
Step 6: Run the erronerous quantum application.
Attacked！

## Slide 71
Results: Quantum Simulator
Lowest Accuracy

## Slide 72
Results: Quantum Hardware
This attack significantly reduces classifier accuracy, undermining the reliability of real quantum hardware.
Here, we utilized a real Noisy Intermediate-Scale Quantum (NISQ) device.
Very Expensive......

## Slide 73
Why MalaQ?
Mala
Quantum
+
=
MALAQ
MALware Attacks Quantum
In this paper, we introduced MalaQ[1], a novel malware targeting vulnerabilities in quantum-classical hybrid computing systems.

## Slide 74
Recently, numerous research findings on QNNs based
on quantum circuit implementations have been proposed
[15–19]. It turns out that the implementation of activation
functions, using quantum circuits, is fundamental and crucial
in QNNs. However, to the best of the authors’ knowledge, there are no dedicated circuit designs for implementing activation functions with a focus on fault tolerance so far.
In this work, we address this gap by constructing a quantum circuit using Clifford+T gates.
Application 1: Q Machine Learning
Quantum Neural Networks (QNNs) represent an intersection between quantum computing and artificial neural networks, hot topic.
Quantum Neural Networks (QNNs)
Activation Function

## Slide 75
Activation Function: Leaky Relu
Simplify it to shifting
{0.125,0.0625,0.03125,0.015625}
{2^-3, 2^-4, 2^-5, 2^-6}
x=0 x=1
T-depth=(n-1)*2*3

## Slide 76
Quantum Trick
The T gate is also known as the pi/4 gate working on a single qubit. Hence, maximum 4
Constant T-Depth=4+4=8
Activation functions are integral components in ml&dl,
providing the crucial non-linearity required for effective learning.

## Slide 77
Application 2: Quantum Cryptography

## Slide 78
Matrix Problem
SubCells
LIGHTER-R only deals at the top level (i.e., Toffoli gates), whereas DORCIS takes quantum decomposition (i.e., Clifford + T gates) into account.

## Slide 79
MixColumn